## Slide 1: MmWave Radar Point Cloud Segmentation using GMM in Multimodal Traffic Monitoring
Feng Jin1, Arindam Sengupta1, Siyang Cao1 and Yao-Jan Wu2
1Department of Electrical and Computer Engineering 2Department of Civil and Architectural Engineering and Mechanics The University of Arizona, Tucson, AZ 85721 Email:{fengjin, sengupta, caos, yaojan}@email.arizona.edu
April 29, 2020

## Slide 2: I. Concept of Multimodal Traffic Monitoring
Provides the real-time traffic statistics, i.e., speed and volume of each transportation mode, such as car, pedestrian, bicycle
To improve the traffic efficiency and reduce crashes
Multimodal Traffic Monitoring System
Advantages of mmWave radar sensor
Robust to adverse weather and poor light (at nights) conditions
Speed measurement through Doppler effect
High bandwidth up to 4 GHz, which leads to 3.75 cm range resolution
Low-cost and compact design
Key problem in this research
How to recognize different traffic modes, such as cars/pedestrians, using mmWave radar sensor
Point cloud segmentation is point-wise classification

## Slide 3: II. What can we get from a mmWave radar sensor?
Assumption: different traffic mode obeys a certain multivariate Gaussian distribution

## Slide 4: III. A new feature vector for each point
Body extent
Relative Doppler
RCS
Original measurement from mmWave radar sensor

## Slide 5: IV. Gaussian Mixture Model (GMM)
Assumption
Feature vector
GMM
Posterior
Maximize a posterior (MAP)
Unknows: Prior and Gaussian statistics of each class
Expectation–maximization (EM) Algorithm

## Slide 6: V. Experiment
Training Dataset
One car driving randomly and one pedestrian walking randomly
8035 radar frames
No labeling (GMM is an unsupervised approach)
Testing Dataset
1222 radar frames
Let a pedestrian walk on the left side of line-of-sight (LOS), in this case y>0
Let a car drive on the right side of LOS, in this case y<0
Label the points with a distinct integer according to its y value. We have ground truth for testing.
Apply GMM on the training dataset
Save the GMM model
Visualize the result to assign GMM output (an integer) to a class
Test the saved GMM model on the testing dataset
Compute performance matrices
Experiment Procedure

## Slide 7: VI. A single frame result
Blue: pedestrian; Green: car; Red: clutter.
Prediction on one frame testing data; (b) The associated ground truth

## Slide 8: VII. Confusion Matrix

## Slide 9: GitHub Repository for Public Access
Thanks!
Q&A
https://github.com/radar-lab/traffic_monitoring